This page was exported from Braindump2go Free Exam Dumps with PDF and VCE Collection [    https://www.mcitpdump.com    ]

Export date: Wed Apr 17 1:55:10 2024 / +0000 GMT

## [2017-Dec-New]Valid 300-360 PDF Dumps Free Download in Braindump2go[Q106-Q115]

2017 December New Cisco 300-360 Exam Dumps with PDF and VCE Free Updated Today! Following are some new 300-360 Exam Questions:

1.|2017 New 300-360 Exam Dumps (PDF & VCE) 140Q&As Download:

https://www.braindump2go.com/300-360.html

2.|2017 New 300-360 Exam Questions & Answers Download:

https://drive.google.com/drive/folders/0B75b5xYLjSSNaFhjTjl4Uk0tbDg?usp=sharing

QUESTION 106

IEEE 802.11r-2008 or fast BSS transition (FT), also called "fast roaming," Which 802.11 standard performs the PTK calculations in advance to enable fast client roaming?

A. 802.1 11r

B. 802.1 11i

C. 802.1 11k

D. 802 1 11w

Answer: A

Explanation:

802.11r, Which is the IEEE standard for fast roaming, introduces a new concept of roaming where the initial handshake with the new AP is done even before the client roams to the target AP, which is called Fast Transition (FT). The initial handshake allows the client and APs to do the Pairwise Transient Key (PTK) calculation in advance. These PTK keys are applied to the client and AP after the client does the reassociation request or response exchange with new target AP.

https://www.cisco.com/c/en/us/td/docs/wireless/controller/technotes/80211r-ft/b-80211r-dg.html

QUESTION 107

Which three factors must you consider before you deploy APs to a wireless network located in a warehouse? (Choose three.)

A. conveyor belts

B. employee schedules

C. ceiling height

D. variable inventory quantities

E. types of walls

F. deliveries

Answer: BCE

QUESTION 108

During a post-deployment survey, the wireless engineer notices that offices in surrounding suites also have wireless networks and the 2.4 Ghz band is highly utilized Which configuration must the engineer make on the wireless network using this new information?

A. Disable 802.11 b/g data rates.

B. Enable Band Sect in the WLC

C. Disable RRM in the WLC.

D. Enable rogue access point containment.

Answer: D

Explanation:

Monitoring Rogue Access Point Alarms

Rogue access point radios are unauthorized access points detected by one or more Cisco lightweight access points.

This page displays rogue access point alarms based on the severity you clicked in the Alarm Monitor.

https://www.cisco.com/c/en/us/td/docs/wireless/mse/3350/5-2/wIPS/configuration/guide/msecg_wIPS/msecg_appB_wIPS.html#wp1244525

QUESTION 109

An engineer must design a wireless voice network and is auditing the existing configuration.

Which two actions must be taken? (Choose two.)

A. Enable Platinum QoS profile on the SSID

B. Disable Coverage Hole Detection.

C. Ensure the switch ports trust DSCP QoS markings

D. Disable WMM on the QoS tab

E. Ensure that Client Load Balancing is enabled.

Answer: AC

Explanation:

https://mrncciew.com/2012/11/28/understanding-wireless-qos-part-1/

QUESTION 110

An engineer is implementing Q0S for a new wireless voice network. Which two considerations should be identified first? (Choose two.)

A. QoS marking

B. policing

C. QoS requirements

D. data traffic usage

E. traffic classification

Answer: CE

QUESTION 111

An engineer is determining powering requirements for a P2P wireless link using Cisco Aironet 1572EC access points.

Which power method is valid for the access point?

A. 802.3af Power over Ethernet

B. Power over Cable

C. Cisco Inline Power

D. 802.3at Power over Ethernet

Answer: B

QUESTION 112

17.A network engineer is performing a site survey in preparation for an installation. Which three hardware parameters must be inspected? (Choose three.)

A. routing protocol used

B. PoE capability

C. switch STP capability

D. distance of antenna to communications room

E. switch port availability

F. distance of access point to communications room

Answer: BEF

QUESTION 113

An engineer has added an access point to a deployment after a post-installation site survey. The engineer then notices that there has been an increase in co-channel interference and retransmissions. Which two features can help mitigate the issue? (Choose two.)

A. Coverage Hole Detection

B. Transmit Power Control

C. Enhanced Distributed Channel Access

D. Cisco Compatible Extensions

E. Dynamic Channel Assignment

Answer: CE

QUESTION 114

You are planning the coverage for wireless VoIP by using Ekahau. Which signal strength does Ekahau recommend using for VoIP?

A. -84 dBm

B. -76 dBm

C. -67 dBm

D. -53 dBm

Answer: C

Explanation:

Each vendor has their own recommended signal strength for a given data rate or application. For instance, one vendor may recommend designing their VoIP solution at -67 dBm (perhaps the most widely-used value for VoIP deployment if I had to choose one), while another may say -70 dBm. In most cases the values will differ only by a couple dB.

https://www.ekahau.com/blog/2015/01/13/ekahau-site-survey-heatmap-visualizations-part-2-signal-stren gth/

QUESTION 115

You must upgrade a data-based wireless network to support Voice over Wireless. Which RSSI measurement do you use to redesign the wireless network?

A. -65 dBm

B. -72 dBm

C. -75 dBm

D. -67 dBm

Answer: D

!!!RECOMMEND!!!

1.|2017 New 300-360 Exam Dumps (PDF & VCE) 140Q&As Download:

https://www.braindump2go.com/300-360.html

2.|2017 New 300-360 Study Guide Video:

YouTube Video: YouTube.com/watch?v=lh_tn49RVms

Post date: 2017-12-08 03:40:37

Post date GMT: 2017-12-08 03:40:37

Post modified date: 2017-12-08 03:40:37

Post modified date GMT: 2017-12-08 03:40:37

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com