This page was exported from Braindump2go Free Exam Dumps with PDF and VCE Collection [    https://www.mcitpdump.com    ]

Export date: Thu Apr 18 14:41:26 2024 / +0000 GMT

## [August-2016-New]Braindump2go 300-209 PDF Book Free Download[NQ11-NQ20]

!!!August 2016 Cisco Official News!!!

CCNP Security 300-209 SIMOS: Implementing Cisco Secure Mobility Solutions (SIMOS) Exam Questions Updated Today!

Instant Free Download 300-209 SIMOS PDF & 300-209 SIMOS VCE Dumps from Braindump2go.com!

100% Pass Guaranteed!

100% Real Exam Questions!

NEW QUESTION 11 - NEW QUESTION 20:

1.|2016/08 Latest 300-209 SIMOS PDF & 300-209 SIMOS VCE 237Q&As: http://www.braindump2go.com/300-209.html

2.|2016/08 Latest 300-209 SIMOS SISAS Exam Questions PDF: https://drive.google.com/folderview?id=0B272WrTALRHcRmVtQ29JNWk3Nzg&usp=sharing

QUESTION 11

A user is unable to establish an AnyConnect VPN connection to an ASA. When using the Real-Time Log viewer within ASDM to troubleshoot the issue, which two filter options would the administrator choose to show only syslog messages relevant to the VPN connection? (Choose two.)

A.    Client's public IP address

B.    Client's operating system

C.    Client's default gateway IP address

D.    Client's username

E.    ASA's public IP address

Answer: AD

QUESTION 12

Which Cisco ASDM option configures forwarding syslog messages to email?

A.    Configuration > Device Management > Logging > E-Mail Setup

B.    Configuration > Device Management > E-Mail Setup > Logging Enable

C.    Select the syslogs to email, click Edit, and select the Forward Messages option.

D.    Select the syslogs to email, click Settings, and specify the Destination Email Address option.

Answer: A

QUESTION 13

Which Cisco ASDM option configures WebVPN access on a Cisco ASA?

A.    Configuration > WebVPN > WebVPN Access

B.    Configuration > Remote Access VPN > Clientless SSL VPN Access

C.    Configuration > WebVPN > WebVPN Config

D.    Configuration > VPN > WebVPN Access

Answer: B

QUESTION 14

A user with IP address 10.10.10.10 is unable to access a HTTP website at IP address

209.165.200.225 through a Cisco ASA. Which two features and commands will help

troubleshoot the issue? (Choose two.)

A.    Capture user traffic using command capture capin interface inside match ip host

10.10.10.10 any

B.    After verifying that user traffic reaches the firewall using syslogs or captures, use packet tracer command

packet-tracer input inside tcp 10.10.10.10 1234 209.165.200.225 80

C.    Enable logging at level 1 and check the syslogs using commands logging enable, logging buffered 1 and

show logging | include 10.10.10.10

D.    Check if an access-list on the firewall is blocking the user by using command show running-config

access-list | include 10.10.10.10

E.     Use packet tracer command packet-tracer input inside udp 0.10.10.10 1234192.168.1.3 161 to see

what the firewall is doing with the user's traffic

Answer: AB

QUESTION 15

A Cisco router may have a fan issue that could increase its temperature and trigger a failure. What troubleshooting steps would verify the issue without causing additional risks?

A.    Configure logging using commands "logging on", "logging buffered 4", and check for fan failure logs

using "show logging"

B.    Configure logging using commands "logging on", "logging buffered 6", and check for fan failure logs

using "show logging"

C.    Configure logging using commands "logging on", "logging discriminator msglog1 console 7", and check

for fan failure logs using "show logging"

D.    Configure logging using commands "logging host 10.11.10.11", "logging trap 2", and check for fan failure

logs at the syslog server 10.11.10.11

Answer: A

QUESTION 16

Which of these are the two types of keys used when implementing GET VPN? (Choose two)

A.    key encryption

B.    group encryption

C.    pre-shared key

D.    public key

E.    private key

F.    traffic encryption key

Answer: AF

QUESTION 17

A private wan connection is suspected of intermittently corrupting data. Which technology can a network administrator use to detect and drop the altered data traffic?

A.    AES-128

B.    RSA Certificates

C.    SHA2-HMAC

D.    3DES

E.    Diffie-Helman Key Generation

Answer: C

QUESTION 18

A company needs to provide secure access to its remote workforce. The end users use

public kiosk computers and a wide range of devices. They will be accessing only an internal web application. Which VPN solution satisfies these requirements?

A.    Clientless SSLVPN

B.    AnyConnect Client using SSLVPN

C.    AnyConnect Client using IKEv2

D.    FlexVPN Client

E.    Windows built-in PPTP client

Answer: A

QUESTION 19

A network administrator is configuring AES encryption for the ISAKMP policy on an IOS router. Which two configurations are valid? (Choose two.)

A.    crypto isakmp policy 10

encryption aes 254

B.    crypto isakmp policy 10

encryption aes 192

C.    crypto isakmp policy 10

encryption aes 256

D.    crypto isakmp policy 10

encryption aes 196

E.    crypto isakmp policy 10

encryption aes 198

F.    crypto isakmp policy 10

encryption aes 64

Answer: BC

QUESTION 20

Which two qualify as Next Generation Encryption integrity algorithms? (Choose two.)

A.    SHA-512

B.    SHA-256

C.    SHA-192

D.    SHA-380

E.    SHA-192

F.    SHA-196

Answer: AB  !!!RECOMMEND!!!

Braindump2go 2016/08 New Cisco 300-209 SIMOS Exam VCE and PDF 237Q&As Dumps Download:

http://www.braindump2go.com/300-209.html [100% 300-209 Exam Pass Promised!]

2016/08 Cisco 300-209 SIMOS New Questions and Answers PDF:

https://drive.google.com/folderview?id=0B272WrTALRHcRmVtQ29JNWk3Nzg&usp=sharing

Post date: 2016-08-03 08:39:29

Post date GMT: 2016-08-03 08:39:29

Post modified date: 2016-08-03 08:39:29

Post modified date GMT: 2016-08-03 08:39:29

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com