This page was exported from Braindump2go Free Exam Dumps with PDF and VCE Collection [    https://www.mcitpdump.com    ]

Export date: Tue Apr 16 6:18:33 2024 / +0000 GMT

## [August-2019-New]Official 300-135 Exam VCE and PDF Offered for Free Download

August/2019 Braindump2go 300-135 Exam Dumps with PDF and VCE New Updated Today! Following are some new 300-135 Real Exam Questions:

1.|2019 Latest Braindump2go 300-135 Exam Dumps (PDF & VCE) Instant Download:

https://www.braindump2go.com/300-135.html

2.|2019 Latest Braindump2go 300-135 Exam Questions & Answers Instant Download:

https://drive.google.com/drive/folders/0B75b5xYLjSSNTFg2a1ZwLUwtNmM?usp=sharing

Real Questions

Which of the following characteristics describe the BPDU Guard feature? (Choose all that apply.)

A. A BPDU Guard port should only be configured on ports with PortFast enabled.

B. BPDU Guard and PortFast should not be enabled on the same port.

C. BPDU Guard is used to ensure that superior BPDUs are not received on a switch port.

D. A BPDU Guard port receiving a BPDU will go into err-disable state.

E. A BPDU Guard port receiving a BPDU will be disabled.

F. BPDU Guard can be enabled on any switch port.

Answer: ADE

Real Questions

Which of the following pieces of information will the command show interface provide? (Choose all that apply.)

A. Layer 1 status

B. Output queue drops

C. Interface CPU utilization

D. Cable type connected to interface

E. Layer 2 status

F. Input queue drops

Answer: ABEF

Real Questions

Which of the following are valid methods of providing a router with information concerning the location of the RP? (Choose all that apply.)

A. Statically defined RP

B. Bootstrap Router

C. Auto-RP

D. RP Discovery Protocol (RDP)

E. RP Helios

F. RPARP(RARP)

Answer: ABC

Real Questions

Which of the following statements regarding documentation would not be considered a helpful step in the troubleshooting process?

A. Use the Cisco Auto Configuration tool.

B. Use the Cisco Rollback feature.

C. Automate documentation.

D. Schedule documentation checks.

E. Use the Cisco Configuration Archive tool.

F. Require documentation prior to a ticket being closed out.

Answer: A

Real Questions

A new router is added to an existing HSRP standby group. One of the existing routers is in an active state, the other is in a standby state. Under what circumstance will the new router become the active router?

A. The new router will become active immediately because it's the newest router introduced into the group.

B. The new router can become active only when the existing active router and the existing standby router become unavailable.

C. The new router has a lower priority value.

D. The new router will never become active unless the existing active router becomes unavailable.

E. The new router has preempt configured and a higher priority

F. The new router has a higher priority value.

Answer: E

Real Questions

Which of the following options represents the correct sequence of DHCP messages after a client initially boots?

A. DHCPREQUEST, DHCPOFFER, DHCPDISCOVER, DHCPACK

B. DHCPDISCOVER, DHCPOFER, DHCPREQUEST, DHCPACK

C. DHCPOFFER, DHCPACK, DHCPREQUEST, DHCPDISCOVER

D. DHCPDISCOVER, DHCPREQUEST, DHCPOFFER, DHCPACK

E. DHCPREQUE5T, DHCPDISCOVER, DHCPOFFER, DHCPACK

F. DHCPDISCOVER, DHCPACK, DHCPREQUEST, DHCPOFFER

Answer: B

Real Questions

Which of the following topology situations would be a qood candidate for configuring DMVPN?

A. Extranet VPN

B. Managed overlay VPN topology

C. Hub-and-spoke VPN topology

D. Central-site VPN topology

E. Full mesh VPN topology

F. Remote-access VPN topology

Answer: E

Real Questions

Which of the following is not a valid reason for a packet to be punted?

A. The TCAM has reached capacity

B. An unknown destination MAC address

C. A packet being discarded due to a security violation

D. A Telnet packet from a session being initiated with the switch

E. Routing protocols sending broadcast traffic

F. A packet belonging to a GRE tunnel

Answer: C

Real Questions

Several troubleshooters are about to work on the same problem. Which of the following troubleshooting methods would be most appropriate to make the best use of the troubleshooters1 time?

A. Bottom up

B. Component swapping

C. Top down

D. Shoot from the hip

E. Divide and conquer

F. Follow the traffic path

Answer: E

Real Questions

You examine the port statistics on a Cisco Catalyst switch and notice an excessive number of frames are being dropped. Which of the following are possible reasons for the drops?

A. Unknown destination MAC address

B. Bad cabling

C. MAC forwarding table is full

D. Port configured for half duplex

E. Port configured for full duplex

F. Network congestion

Answer: BF

Real Questions

Which of the following is a valid host IPv6 address? (Choose all that apply.)

A. ff02:a:b:c::l/64

B. 2001:aaaa: 1234:456c: 1/64

C. 2001:000a:lb2c::/64

D. 2fff:f:f:f::f/64

E. ff02:33ab:l:32::2/128

F. 2001:bad:2345:a:b::cef/128

Answer: BF

Explanation:

Option B is valid, assuming theres a faulty colon : in the IPv6 Address, just before the last 1, that is: 2001:aaaa:1234:456c::1/64Option F is valid, dispite its odd network mask (128 bits), sometimes used in tunnel links.

Incorrect answer:

Option A is invalid, since it is a Multicast addressOption C seems to be invalid because the 3rd group of characters includes an l (lb2c), but if it is a 1 instead of an l (faulty scan) and the required options are 3 instead of 2, then this address is still valid (2001:000a:1b2c::/64), because the 4th group of characters would be 0000 (remember that we can represent a continuous sequence of zeros by ::).Option D is definitely invalid since it is a reserved address. As states the IANA online :document about the IPv6 Unicast Global Addresses, the range below is reserved, not allocated to any RIR (Regional Internet Registry):

2E00:0000::/7 IANA 1999-07-01 RESERVED

!!!RECOMMEND!!!

1.|2019 Latest Braindump2go 300-135 Exam Dumps (PDF & VCE) Instant Download:

https://www.braindump2go.com/300-135.html

2.|2019 Latest Braindump2go 300-135 Study Guide Video Instant Download:

YouTube Video: YouTube.com/watch?v=k-eQ0XsVPto

" href="https://youtu.be/k-eQ0XsVPto">

YouTube Video: YouTube.com/watch?v=k-eQ0XsVPto

Post date: 2019-08-02 07:33:23

Post date GMT: 2019-08-02 07:33:23

Post modified date: 2019-08-02 07:33:23

Post modified date GMT: 2019-08-02 07:33:23

Powered by [ Universal Post Manager ] plugin. MS Word saving format developed by gVectors Team    www.gVectors.com